DatabaseID=4E35412F20205455525C5320|ContactID=3E524321202049202B582321|January 3, 2007	                                                                         PROPOSAL: 6352

Robert Robertson	Phone:	574-555-4321

1854 Acorn Lane 	Fax:	574-555-8765

Mishawaka, IN  46544	Project Location:	Same

We propose to furnish all labor, material and equipment to complete the following:

Item #1 Replace drive 18'- 6'' x 38' with 5' x 8' walk

150 Mob & De Mob

202 Demo Drive

- Provide and maintain barricades during construction

- Saw cut and remove existing concrete

312 Install Drive

- Dowell 3/8'' rod into existing concrete at 24'' on center

- Install concrete 4'' thick with wire mesh reinforcement

- Apply concrete curing after finishing