### Standard Flatwork Specifications Sheet

Removal of existing materials: Unless stated otherwise, all existing materials that need to be removed in order to accommodate the installation of concrete will be hauled away to an approved dump site. Removal of existing concrete is based on the concrete being 4" thick. If thicker concrete is encountered, there will be an additional cost for removal. You will be notified before this work continues as to what the cost could be.

Existing soils: Unless poor soil conditions are obvious and addressed on the Proposal, L.L. Geans Construction Co. estimates the proposed work based on acceptable soil conditions. When the crew comes out to do your work, our men will check the soils with a rod to determine if there are any major soil problems, or poor compaction. This rod will only test about 2' deep.  If there is any indication that poor soils exist, or if the soil is not compacted, you will be notified.  Any removal and installation of acceptable materials will be additional.

Compaction: Upon final grading, L.L. Geans Construction Co. will operate a vibratory plate compactor over the entire area. This compactor only handles the top 3" to 4", and no more.

Steps and Railings: All steps will meet all codes for riser height and tread depth.  Risers will not vary in height with each other more than ¼”.  All risers will have a 3/8” rebar mat installed in concrete.  If railing is included in the proposal, installation will be done after the concrete is poured and has been allowed to cure for 14 days

Edges of Driveways: All edges of driveways to be thickened to 5”, and receive a continuous 3/8” rod.  This builds a miniature concrete grade beam and provides a great deal of support.

Connection to existing concrete: 3/8’ rods will be installed into adjoining existing concrete to minimize movement and consequent elevation change between the new and existing flatwork concrete.  3/8” rods will be installed at the bottom of the new concrete into adjoining concrete foundation walls, allowing concrete to move up if needed and preventing any settling against such walls.

Concrete mix design: All exterior concrete will be either 6 bag limestone mix or 4,000 PSI limestone mix.

Joints: Expansion and control joints will be installed according to recommendations by the American Concrete Institute. Expansion will be black 1/2" material located in areas to help minimize cracking. Control joints will be installed during the finishing process, or sawcut immediately after concrete has cured sufficiently.

Care and cleanup of your Property: L.L. Geans Construction Co. is extremely careful around your property and lawn.  We always do a thorough clean up, so that it looks as though we have never been on your property. If for any reason we have to put any equipment on your property we will always fill in low areas with materials that match existing area.. You would be responsible for watering, and maintenance. In areas where we used forms, we will install topsoil from edge of concrete to your existing lawn or grade, and install seed. You will be responsible for watering and maintenance.

Curing:   All concrete will receive an application of concrete curing immediately after the finishing process has been completed. We recommend that you apply a concrete sealer every fall for additional protection from freeze thaw cycle and de-icers.

Reinforcement: All patios and walks will receive 6" x 6", 10/10 gauge wire mesh throughout, and all driveways will receive a mat of  3/8” rebar 18” on center each way with the exception of work done in city right of ways. It is a requirement in South Bend and Mishawaka that city right of ways have no steel reinforcement in concrete. This is usually 10' to 20' from edge of road.

Permits:   Unless noted, L.L. Geans Construction Co will obtain all necessary permits for your concrete project.  The costs are included in your proposal.

Thickness:   Unless noted, all concrete will be 4" thick.   Approaches and city walks at approach areas will be 6" thick.

Your concrete flatwork has been designed at 4” for light vehicular traffic; i.e. passenger cars, pickups, light passenger vans, etc; If you think that your concrete may in the future ever experience heavier loads than light vehicular traffic, please provide us with the type of traffic you might anticipate and we will be happy to provide an alternate quote for a design to meet those loads.

The concrete work we are having installed by L.L. Geans Construction will receive light vehicular traffic only, and no other heavier loads.								                                    Initials_________

I think this concrete may experience heavier loads than those described for light vehicular traffic and I would like to have a price on concrete that will handle the following types of traffic and loads:______________________________________________________________________________________________________________________________________________________________________________     Initials_________

Sprinkler Lines: The past 25 years have seen a dramatic increase of sprinkling systems. They present a challenge for L.L. Geans when we are driving stakes in the ground for forms. In a nutshell, the problem is that we are not able to locate the existing sprinkling lines unless we excavate everywhere we thought they might exist. This brings us to five (5) options:

- You, the owner, hand dig and locate all lines near our work marking the line 2' on center with flags.

- Your sprinkler contractor comes out and marks the lines.

- L.L. Geans Construction Co. excavates and marks the lines at a cost of $50.00 per hour for the time needed and any materials required.

- L.L. Geans forms the work and drives stakes as needed. After work is completed, your sprinkler contractor pressure checks or runs the sprinklers to check for any damaged lines.

- Install your flatwork smaller than  existing concrete by approximately 2-1/2” on each side avoiding existing lines.

Important:  L.L. Geans Construction Co. is not responsible for any costs to repair sprinkler systems damaged in Option #4, or damage to unmarked lines in option 1 & 2.  Unfortunately, there are times that we must remove a head or line to facilitate the construction and we never know until we are working on the project.  Costs associated with the repairs of these lines will be additional.

Please select the option that you would like for the sprinkler lines as noted above. Option No:____  Initials ________

Sprinkling system not present in the work area.        Initials________

Buried Utilities: L.L. Geans Construction Co. will call Indiana Underground to mark wires and pipes three days before work begins. Indiana Underground only marks the service lines that supply the particular utility. Any and all other secondary lines within your property is your responsibility.  L.L. Geans Construction Co. is not responsible for loss or damage to unmarked wires, pipes, utility lines, etc. It’s very important that you the owner make us aware of any lines buried, overhead, or near the proposed construction area, and that these lines are marked by you or your utility contractor.                                                                                                                                                                       							There are no utilities that I am aware of.       Initials ________

There are utilities and I have marked them with paint or flags and identified what they are below. Initials ________

___________________________________________________________________________________________________

I understand and agree to all the Specifications and Qualifications listed above.

___________________________________________________________________________________________________

Signature				Print Name				Date

Comments from Owner:

Please list any concerns that we need to be aware of before work begins on your project.